## Slide 1
Thomas Bialas, (566)
Yen Wong (566)
Peter Fetterer (566)
Salem El-Nimri (566, ASRC)
Deepak Kaul (566, ASRC)
Mark Sinkiat (566, ASRC)
Near Earth Network Gateway
Phase II
Systems Requirements Review
July 8, 2015

## Slide 2: Agenda
Introduction
Overview
Operations Concept
Requirements
  SRD 3.1 Operations
  SRD 3.2 Performance
  SRD 3.3 RMA
  SRD 3.4 Security
  SRD 3.5 Contingency
  SRD 3.5 Standards
  RTVM
Risks
Conclusion
Questions

## Slide 3
Introduction

## Slide 4: Purpose
Examines the functional and performance requirements defined for the NENG Phase II system and ensures that the requirements and concept will satisfy customer needs.
Objectives
  Baseline mission requirements are clearly understood
  Top-level requirements for each system element have been determined
  Proposed mission design and operations concept satisfies baseline mission requirements
  Plans for future activities justify expectations the mission design will accommodate
  Imposed constraints and accomplish the mission within allocated resources
  Get feedback from the SRR review panel and participants to ensure the NENG Phase II requirements set is appropriate, complete and well defined

## Slide 5: SRR Board
Review Chair:
  Philip Baldwin, Telecommunications , Code 566
Review Member:
  Serhat Altunc, Telecommunications, Code 566
Review Member:
  Obadiah Kegege, Telecommunications, Code 566
Review Member:
  Dave Sohl, Flight Systems Test, Code 568

## Slide 6: Request for Action and Action Items
Request for Action (RFA)
  RFAs should be significant enough to report to management
  RFAs may be written by anyone
  The review board will meet immediately following the review, assess RFA validity, and provide initial copy of the RFA
  The NENG PDL will assign accepted RFAs to team members for response and action
  RFA responses will be prepared by the assignee and coordinated with the originator for their acceptance or rejection
  RFAs need to be related to the SRR scope and not design changes
Action Item (AI)
  AI’s will be used for items that do not rise to the level of an RFA
  AI’s will be captured throughout the review

## Slide 7: Current Org Chart
Lead Software Engineer
Lead Test Engineer
Ops
Network Engineer
Product Development Lead (PDL)
SCNS
Systems Engineer
Deputy PDL
Hardware Engineer

## Slide 8: Entry Criteria
sehb srr ee
Successful completion of the MCR and responses made 1. to all MCR RFAs and rids
2. A preliminary SRR agenda, success criteria, and charge to the board have been agreed to by the technical team, project manager, and review chair prior to the SRR.
agreed to by the technical team, project manager, and review chair prior to the SRR.
3. The following technical products for hardware and software system elements are available to the cognizant participants prior to the review:
a. system requirements document;
b. system software functionality description;
c. updated ConOps;
d. updated mission requirements, if applicable;
e. baselined SEMP;
f. risk management plan;
g. preliminary system requirements allocation to the next lower level system;
h. updated cost estimate;
i. technology development maturity assessment plan;
j. updated risk assessment and mitigations (including PRA, as applicable);
k. logistics documentation (e.g., preliminary maintenance plan);
l. preliminary human rating plan, if applicable;
m. software development plan;
n. system SMA plan;
o. CM plan;
p. initial document tree;
q. verification and validation approach;
r. preliminary system safety analysis; and
s. other specialty disciplines, as required.
The project utilizes a sound process for the allocation and control of requirements throughout all levels, and a plan has been defined to complete the definition activity within schedule constraints.
2. Requirements definition is complete with respect to top-level mission and science requirements, and interfaces with external entities and between major internal elements have been defined.
3. Requirements allocation and flowdown of key driving requirements have been defined down to subsystems.
4. Preliminary approaches have been determined for how requirements will be verified and validated down to the subsystem level.
5. Major risks have been identified and technically assessed, andviable mitigation strategies have been defined.

## Slide 9: Success Criteria
The project utilizes a sound process for the allocation and control of requirements throughout all levels, and a plan has been defined to complete the definition activity within schedule constraints.
2. Requirements definition is complete with respect to top-level mission and science requirements, and interfaces with external entities and between major internal elements have been defined.
3. Requirements allocation and flowdown of key driving requirements have been defined down to subsystems.
4. Preliminary approaches have been determined for how requirements will be verified and validated down to the subsystem level.
5. Major risks have been identified and technically assessed, andviable mitigation strategies have been defined.

## Slide 10: Entrance Criteria
Entrance Criteria | Comment
A Formulation Authorization Document (FAD) has been approved. | N/A
Program requirements have been defined that support mission directorate requirements on the program. | 
Major program risks and corresponding mitigation strategies have been identified | 
The high-level program requirements have been documented to include: Performance Safety, and Programmatic requirements | 
An approach for verifying compliance with program requirements has been defined | 
Procedures for controlling changes to program requirements have been defined and approved | 
Traceability of program requirements to individual projects is documented in accordance with Agency needs, goals, and objectives, as described in the NASA Strategic Plan | 
Top program/project risks with significant technical, safety, cost, and schedule impacts are identified | 

## Slide 11
Overview

## Slide 12: NENG Phase II Overview
Ground Station
WSGT
ASF
WFF
Cortex HDR XXL
NENG
Customer
RF Link
Telemetry Stream
NISN
Telemetry Files
TCP/ IP (SSH-SCP)
TCP/ IP
Scheduling
M&C
File

## Slide 13: Current Architecture
Provides NEN ground station users with automated 24/7 near-real time files based IP access to spacecraft telemetry data
  NENG is composed of 4 servers (2 prime, 2 cold spares), 2 RAIDs and custom applications written in C++
  Pass Telemetry and Accounting from receiver is captured in 1 minute (nominal) files on closed system.
  Pass Telemetry and Accounting files are delivered via SCP to user facilities from closed system
  Open system is updated with Telemetry and Accounting files from closed system

## Slide 14: Current Capabilities
NENG has been lab tested to 600 Mbps ingest rate, and supports IRIS at 13.125 Mbps.
File delivery rates depend on WAN speeds connecting to user sites
All files are stored for at least 7 days (nominal) and are user retrievable from the open system
  10TB of storage nominal, easily expandable

## Slide 15: Current Proficiency
NENG IRIS mission performance
  0 data loss and 0 operations failures since IRIS Launch (27June13)

## Slide 16: Current Status
New Cortex HDR XXL was received
All servers and RAIDs for phase II are in house
Initial design trade studies were discussed for auto failover implementation
Draft documentation
  See Documentation Tree
Configuration management system and plan are in place
Software development management plan is in place

## Slide 17
Operations Concept

## Slide 18: Phase II Operations Concept
The NENG System will receive a conflict free schedule from Near Earth Network Scheduling Engine (NENSE)
  The system will automatically configure and run accordingly
  The system can be interrupted in the event of an emergency
    The system can be operated through M&C control
In the event of a failure, the system will perform an auto failover to the back up units
The NENG System will provide status information to operations
The NENG captures a telemetry stream into telemetry files for delivery in near-real time to missions via Secure Copy (SCP)
  The mission has the ability to retrieve telemetry files within an agreed amount of time via Secure File Transport (SFTP)
  The files are held for an agreed amount of time before they are purged from the system

## Slide 19
Requirements

## Slide 20: Top Level Requirement
NENG shall provide NENG ground station users with automated 24/7 near real time file based spacecraft telemetry data
Phase II Driving Requirements
  The NENG shall provide auto failover capabilities
  The NENG shall ingest spacecraft telemetry data at 1Gbps
  The NENG shall run automatically based on an ingested NENSE (Near Earth Network Schedule Engine) schedule file (M&C is status only)
Deliver all gateway systems with Enhanced Linux version
  WGS (1 system)
  AS1, AS2, AS3 (3 systems)
  WS1 (1 system)

## Slide 21: SRD 3.1 - Operations
Id | Requirement | Phase
NENG-OPS-001 | The NEN Gateway shall provide automated delivery of user data to authorized users | 
NENG-OPS-002 | The NEN Gateway shall attempt automated delivery once | 
NENG-OPS-004 | The NEN Gateway shall operate unattended | 
NENG-OPS-005 | The NEN Gateway shall report warning and erroneous conditions to the operator interface | 
NENG-OPS-020 | The NEN Gateway shall store at least 10TB of combined mission data | 
NENG-OPS-021 | The NENG storage system shall be single fault tolerant | 
NENG-OPS-022 | The NENG shall host an access controlled file system | 
NENG-OPS-013 | The NENG shall provide system status | 
NENG-OPS-013.1 | The NEN Gateway storage system shall report: the total storage available for secure/open, total storage used for secure/open, disk health for secure/open, storage system health. | 

## Slide 22: SRD 3.1 - Operations
Id | Requirement | Phase
NENG-OPS-023 | The NENG shall receive, process, and execute schedule files from NENSE | New
NENG-OPS-024 | The NEN Gateway shall provide status via a TCP/IP for remote monitoring | 
NENG-OPS-015 | The NEN Gateway shall be remotely configurable via TCP/IP | 
NENG-OPS-016 | The NEN Gateway shall provide a system logging function to log system failure and operational activity | 
NENG-OPS-019 | The NENG storage systems shall operate in a computer room environment | 

## Slide 23: SRD 3.2 - Performance
Id | Requirement | Phase
NENG-PERF-001 | The NEN Gateway shall respond to commands from the remote TCP/IP interface in less than 5 seconds | 
NENG-PERF-002 | For NENSE scheduled supports the NENG shall execute setup for support 120 seconds prior to activity scheduled start time | 
NENG-PERF-010 | The NEN Gateway shall receive and process at a data rate of up to 1 Gbps | New
NENG-PERF-009 | From ingest to the LAN to the delivery of IP files to the LAN, the latency shall not exceed 3 minutes for nominal operations | 

## Slide 24: SRD 3.2 - RMA (Reliability, Maintainability, and Availability)
Id | Requirement | Phase
NENG-RMA-016 | The NEN Gateway data processing/ delivery system shall have a reliability of 95% between maintenance cycles for nominal operational condition | 
NENG-RMA-017 | The NEN Gateway data storage system shall have a reliability of 90% between maintenance cycles for nominal operational condition | 
NENG-RMA-018 | The NEN Gateway degraded mode data processing/ delivery system shall have a reliability of 90% between maintenance cycles | 
NENG-RMA-005 | The NEN Gateway nominal data processing/ delivery system shall have an availability of 0.9999 for scheduled support periods | 
NENG-RMA-006 | The NEN Gateway degraded mode data processing/ delivery system shall have a delivery availability 0.9 when delivery can be made | 

## Slide 25
Id | Requirement | Phase
NENG-RMA-009 | The NEN Gateway data processing/ delivery system shall have a Mean Time Between Failures (MTBF) not less than 12,000 hours | 
NENG-RMA-019 | The NEN Gateway shall comply with the NEN’s availability requirements | 
NENG-RMA-015 | The NEN Gateway’s Mean Time To Restore Function (MTTRF) shall be less than or equal to 48 hours | 
SRD 3.2 - RMA (Reliability, Maintainability, and Availability)

## Slide 26: SRD 3.3 - Security
Id | Requirement | Phase
NENG-SEC-001 | The NEN Gateway shall provide audit trail capability in compliance with NPR 2810.1A, Section 4.2, Audit Trail and Accountability Requirements | 
NENG-SEC-002 | The NEN Gateway shall support security functions implemented by NEN Systems in compliance with NPR 2810.1A Security of Information Technology when providing interfaces and communications services to other NEN Systems and customers | 
NENG-SEC-003 | The NEN Gateway shall adhere to the security requirements specified in the 700-DOC-029, NASA Integrated Services Network (NISN) Internet Protocol Operational Network (IONet) Security Policy, Section 3 IONet Policies and Security Requirements | 
NENG-SEC-004 | The NEN Gateway shall use security controls, including user access and authentication controls, as specified in NIST SP 800-53, Recommended Security Controls for Federal Information Systems and Organizations, Appendix F: Security Control Catalog, High Impact Baseline, and NPR 2810.1A, Security of Information Technology | 

## Slide 27: SRD 3.3 - Security
Id | Requirement | Phase
NENG-SEC-005 | The NEN Gateway components shall be configured using NASA’s operating system and application configuration benchmarks, as specified in, NIST SP 800-53, Recommended Security Controls for Federal Information Systems and Organizations | 
NENG-SEC-006 | The NEN Gateway shall implement authentication for data transfer services invoked by external users | 
NENG-SEC-007 | The NEN Gateway shall support identification and authentication of network devices prior to connection | 
NENG-SEC-009 | The NEN Gateway shall support peer entity authentication structures | 
NENG-SEC-010 | The NEN Gateway shall provide access enforcement mechanisms such as Access Control Lists to control access between users and/or processes acting on behalf of users on interconnected systems | 

## Slide 28: SRD 3.3 - Security
Id | Requirement | Phase
NENG-SEC-011 | The NEN Gateway shall provide a system logging function to log user access and authentication | 
NENG-SEC-012 | The NEN Gateway shall provide a system logging function to log configuration modifications | 

## Slide 29: SRD 3.4 - Contingency
Id | Requirement | Phase
NENG-ServAssure-005 | The NENG shall automatically handle failover from prime system to the backup system in the event of a primary system failure | New
NENG-ServAssure-006 | The NENG shall notify the operator in the event of an auto failover occurred | New
NENG-ServAssure-003 | The NEN Gateway shall continue to process return data as usual and record it for future delivery self-service in the event that a delivery connection to the MOC is not established | 
NENG-ServAssure-004 | The NENG shall account for each file delivery attempt | 
NENG-ServAssure-007 | The NENG shall support emergency interrupts. i.e. be reconfigurable at any time, even during and active event | 

## Slide 30: SRD 3.5 - Standards
Id | Requirement | Phase
NENG-STD-002 | The NEN Gateway shall use the NEN Time and Frequency Subsystem for all NEN Gateway functions that require time and frequency referencing | 
NENG-STD-004 | The NEN Gateway shall use Coordinated Universal Time (UTC) for all parameters containing a time value | 
NENG-STD-006 | The NEN Gateway shall interface with the NEN Timing Subsystem to maintain internal time traceable to Coordinated Universal Time | 
NENG-STD-007 | The NEN Gateway shall interface with the NEN Timing Subsystem to receive Simple Network Timing Protocol (sNTP) | 

## Slide 31: Requirements Traceability and Verification Matrix
Id | Method | Parent Requirement
NENG-OPS-001 | T - Test | NEN1173
NENG-OPS-002 | T - Test | NEN668
NENG-OPS-004 | T - Test | NEN326
NENG-OPS-005 | T - Test | NEN326
NENG-OPS-020 | I - Inspection | NEN663
NENG-OPS-021 | I - Inspection | NEN336
NENG-OPS-022 | I - Inspection | NEN319
NENG-OPS-013 | T - Test | NEN326
NENG-OPS-013.1 | T - Test | NEN326
NENG-OPS-023 | T - Test | NEN347
NENG-OPS-024 | T - Test | NEN331/ NEN347
NENG-OPS-015 | T - Test | NEN347
NENG-OPS-016 | T - Test | NEN326
NENG-OPS-019 | A - Analysis | Vary by facility

## Slide 32: Requirements Traceability and Verification Matrix
Id | Method | Parent Requirement
NENG-PERF-001 | T - Test | NEN347
NENG-PERF-002 | T - Test | NEN1138
NENG-PERF-010 | T - Test | NEN595
NENG-PERF-009 | T - Test | NEN1138
NENG-RMA-016 | A - Analysis | NEN336
NENG-RMA-017 | A - Analysis | NEN336
NENG-RMA-018 | A - Analysis | NEN336
NENG-RMA-005 | A - Analysis | NEN336
NENG-RMA-006 | A - Analysis | NEN336
NENG-RMA-009 | A - Analysis | NEN336
NENG-RMA-019 | A - Analysis | NEN336
NENG-RMA-015 | A - Analysis | NEN336

## Slide 33: Requirements Traceability and Verification Matrix
Id | Method | Parent Requirement
NENG-SEC-001 | I - Inspection | NEN319
NENG-SEC-002 | I - Inspection | NEN319
NENG-SEC-003 | I - Inspection | NEN319
NENG-SEC-004 | I - Inspection | NEN319
NENG-SEC-005 | I - Inspection | NEN319
NENG-SEC-006 | T - Test | NEN319
NENG-SEC-007 | T - Test | NEN319
NENG-SEC-009 | T - Test | NEN319
NENG-SEC-010 | T - Test | NEN319
NENG-SEC-011 | T - Test | NEN326/331
NENG-SEC-012 | T - Test | NEN326/331

## Slide 34: Requirements Traceability and Verification Matrix
Id | Method | Parent Requirement
NENG-ServAssure-005 | T - Test | NEN336
NENG-ServAssure-006 | T - Test | NEN331
NENG-ServAssure-003 | T - Test | NEN663
NENG-ServAssure-004 | T - Test | NEN326
NENG-ServAssure-007 | T - Test | NEN1173
NENG-STD-002 | I - Inspection | NEN1008
NENG-STD-004 | I - Inspection | NEN1008
NENG-STD-006 | I - Inspection | NEN1008
NENG-STD-007 | I - Inspection | NEN1008

## Slide 35
Risks

## Slide 36: Risks Matrix
1
Likelihood
Consequence
Approach
M – Mitigate
W – Watch
A – Accept
R – Research
Risk
High
Med
Low
L x C Trend
 Decreasing (Improving)
 Increasing (Worsening)
Unchanged
New risk
Index | Rank | L x C Trend | Approach | Risk Title
1 | 10 | è | W | SLE Requirements Addition
1 2 3 4 5
1 2 3 4 5

## Slide 37: Major Risks and Mitigation Strategies
Risk | Mitigation
SLE requirements addition | update schedule, cost, and resources

## Slide 38: NENG Documentation
Interface Control Document
NENG User’s Guide
NENG Test Plan & Procedures
LINUX NENG Users Guide
NEN-UserGuide-0001
Test Procedure
NEN-TP-0001
Configuration management plan
NEN-CM-0001
Integration & Acceptance Plan & Procedures
NENG Management
Assigned
Draft
Signed
NEN ICD Between NENG and IRIS MOC
453-ICD-IRIS/NENGG
100%
Updated
Test Plan for the NENG Phase II
NEN-Plan-0001
100 %
Test Report
NEN-Report-0001
Software Management Plan
NEN-SMP-0001
Concept of Operation
NEN-COP-0001
Note:
We decided to merge the SEMP, Risk management plan, Software function description in The Software management plan
95 %
95 %
50 %
50 %
0 %
75 %
NEN ICD Between NENG and M&C
453-ICD-MC-001
95 %
Requirement Specification Phase II
NEN-REQT-0001
95 %
100 %

## Slide 39: Requirement Management
The NENG Phase II System Requirement Document (SDR) will be under the Configuration Management of Code 453 NEN Project Configuration Control Board (CCB)
A Document Change Notice (DCN) will be issued to update the document for any approved changes The other documents will be maintained under the SCNS configuration management

## Slide 40: NENG Project Schedule
Stage | Date
SRR | 07/08/2015
PDR | 09/30/2015
CDR | 01/12/2016
Pre-Ship/ TRR | 04/20/2016
WFF ORR | 06/09/2016
WSGT ORR | 07/25/2016
ASF ORR | 09/20/2016

## Slide 41
Conclusion

## Slide 42: Success Criteria
Success Criteria | Comment
With respect to mission and science requirements, defined high-level program requirements are determined to be complete and are approved | 
Defined interfaces with other programs are approved | 
The program requirements are determined to provide a cost-effective program | 
The program requirements are adequately levied on either the single-program project or the multiple projects of the program | 
The plans for controlling program requirement changes have been approved | 
The approach for verifying compliance with program requirements has been approved | 
The mitigation strategies for handling identified major risks have been approved | 

## Slide 43: Summary and Conclusion
Ready to start preliminary design activities
The development team is ready to evaluate various trade study options
Pending approval, purchase orders will be placed for the remaining hardware and software needed
  Only Racks and cables remaining

## Slide 44
Questions?