## Slide 1
Salem El-Nimri (566, ASRC)
Deepak Kaul (566, ASRC)
Mark Sinkiat (566, ASRC)
Martin Perrine (567)
Near Earth Network Data Acquisition Processing Handling Environment
Delta Systems Requirements Review
September 2016

## Slide 2: Agenda
Introduction
Overview/Background
Entry Success Criteria
Operations Concept
Requirements Highlights
RTVM
Changes to Requirements
Risks
Conclusion
Questions

## Slide 3
Introduction

## Slide 4: SRR Board
Kenneth Wagner (564, Chair)
–Bruce Thoman (453)
–David Sohl (568)
–Vuong Ly(583)

## Slide 5: Purpose
Examines changes to the functional and performance requirements defined for DAPHNE .
Ensures that the requirements and concept will still satisfy customer needs.
Objectives from SRR
  Baseline mission requirements are clearly understood.
  Proposed mission design and operations concept satisfies baseline mission requirements.
  Plans for future activities justify expectations the mission design will accommodate.
  Imposed constraints and accomplish the mission within allocated resources.
  Get feedback from the SRR review panel and participants to ensure the requirements set is appropriate, complete and well defined.
  Ensure a thorough review of the products supporting the review.
  Ensure the products meet the entrance criteria and success criteria.
  Ensure issues raised during the review are appropriately documented and resolved.

## Slide 6: Request for Action and Action Items
Request for Action (RFA)
  RFAs should be significant enough to report to management.
  RFAs may be written by anyone.
  The review board will meet immediately following the review, assess RFA validity, and provide initial copy of the RFA.
  The DAPHNE PDL will assign accepted RFAs to team members for response and action.
  RFA responses will be prepared by the assignee and coordinated with the originator for their acceptance or rejection.
  RFAs need to be related to the SRR scope and not design changes.
  The items will be vetted through the review chair.
Action Item (AI)
  AI’s will be used for items that do not rise to the level of an RFA.
  AI’s will be captured throughout the review.
  The items will be vetted through the PDL.
Recommendations will also be accepted and considered by the PDL.

## Slide 7: Current Org Chart
Lead Software Engineer
Lead Test Engineer
Ops
Network Engineer Advisor
Product Development Lead (PDL)
SCNS
Systems Engineer
Deputy PDL
Hardware Engineer

## Slide 8: SRR Entrance Criteria System Engineering Handbook
1. Successful completion of the MCR and responses made 1. to all MCR RFAs and rids | By mission
2. A preliminary SRR agenda, success criteria, and charge to the board have been agreed to by the technical team, project manager, and review chair prior to the SRR. | yes
3. The following technical products for hardware and software system elements are available to the cognizant participants prior to the review: | yes
a. system requirements document; | yes
b. system software functionality description; | yes
c. updated ConOps; | yes
d. updated mission requirements, if applicable; | yes
e. baselined SEMP; | yes
f. risk management plan; | yes
h. updated cost estimate; | yes
i. technology development maturity assessment plan; | yes
j. updated risk assessment and mitigations (including PRA, as applicable); | yes
k. logistics documentation (e.g., preliminary maintenance plan); | yes
m. software development plan; | yes
o. CM plan; | yes
p. initial document tree; | yes
q. verification and validation approach; | yes

## Slide 9
Entry criteria either not applicable or we are not doing.
Success criteria we are not doing.
Requirements allocation and flowdown of key driving requirements have been defined down to subsystems.
DO NOT USE For DSRR
g. preliminary system requirements allocation to the next lower level system;
l. preliminary human rating plan, if applicable;
n. system SMA plan;
r. preliminary system safety analysis; and
s. other specialty disciplines, as required.

## Slide 10: SRR- Entrance Criteria DO NOT USE For DSRR
Entrance Criteria | Comment
A Formulation Authorization Document (FAD) has been approved. | N/A
Program requirements have been defined that support mission directorate requirements on the program. | 
Major program risks and corresponding mitigation strategies have been identified | 
The high-level program requirements have been documented to include: Performance Safety, and Programmatic requirements | 
An approach for verifying compliance with program requirements has been defined | 
Procedures for controlling changes to program requirements have been defined and approved | 
Traceability of program requirements to individual projects is documented in accordance with Agency needs, goals, and objectives, as described in the NASA Strategic Plan | 
Top program/project risks with significant technical, safety, cost, and schedule impacts are identified | 

## Slide 11
Overview

## Slide 12: DAPHNE Overview
Ground Station
WSGT
ASF
WFF
IF receiver
DAPHNE
Customer
IF Link
Telemetry Stream
NISN
Telemetry Files
TCP/ IP (SSH-SCP)
TCP/ IP
GS Timing
M&C

## Slide 13: Updated Architecture
Improved security protocols simplify the architecture, avoiding costly open side hardware in previous architecture. See backup slides showing SRR version.

## Slide 14: Current Capabilities
NENG has been lab tested to 600 Mbps ingest rate, and supports IRIS at 13.125 Mbps.
File delivery rates depend on WAN speeds connecting to user sites
All files are stored for at least 7 days (nominal) and are user retrievable from the open system
  28TB of storage is required but the design supports expansion

## Slide 15: Current Proficiency
NENG IRIS mission performance
  0 data loss and 0 operations failures since IRIS Launch (27June13)
  Two new units recently delivered to ASF.
SDO mission support for x years.

## Slide 16: Current Status
Migrated interface from Cortex HDR XXL to Viasat VHR-3200. Basic interface has been tested.
Servers and RAID options are being studied.
Initial design trade studies were discussed for auto failover implementation.
Documentation- see Tree slide.
Configuration management system and plan are in place.
Software development management plan is in place.

## Slide 17
Operations Concept

## Slide 18: DAPHNE Operations Concept
The system will automatically configure by simple M&C command and run accordingly.
The system captures a telemetry stream and converts it into virtual channel telemetry files for delivery in near-real time to missions via Secure Copy (SCP).
  The files are stored for an agreed amount of time before they are purged from the system.
The mission has the ability to retrieve telemetry files via Secure File Transport (SFTP).
The system will provide status information to operations.
Operations can be interrupted and reconfigured in the event of an emergency for higher priority mission.
In the event of a failure, the system will perform an auto failover to back up units.

## Slide 19
Requirements

## Slide 20: Requirements Status
NENG Phase II passed SRR June 2015
NENG renamed DAPHNE
Various meetings held between DAPHNE, NEN and NISAR that indicated the need to revise the requirements.
  Increased rates to 2x2 Gbps
  Send data files in priority order
  Remove scheduled operations
  Add SLE mode
  Simplify RMA requirements
Updates presented with minimal changes.
Most requirements received the NENG to DAPHNE name change.
Added rationale and traceability matrix.
The link for the SRD with full set of requirements is here.
The link for the corresponding RTVM is here.

## Slide 21: Requirement Removed
One requirement about scheduling to remove.
This removal implies small changes in wording to a couple of other requirements (see “Minor Changes”)
The understanding is that the M&C will perform the scheduling function and send explicit operational commands to DAPHNE e.g. Start, Stop, Setup, etc.
Requirement Number | Old Requirement | New Action
NENG-OPS-023 | The NENG shall receive, process, and execute schedule files from NENSN. | Removed

## Slide 22: Requirements Changed
NISAR mission has increased its data volume and corresponding rate.
There are two requirements to change related to these increases.
Requirement Number | Old Requirement | New Requirement
NENG-OPS-020 | The NEN Gateway shall store at least 10 TBytes of combined Missions data. | DAPHNE shall store at least 28 TBytes of combined Mission data.
NENG-PERF-010 | The NEN Gateway shall receive and process at a data rate of up to 1 Gbps. | DAPHNE shall receive and process two streams of telemetry data at a rate up to 2 Gbps each.

## Slide 23: Added Requirements
There are two added requirements
  SLE
  Priority order data transmission
Requirement Number | Old Requirement | New Requirement
Not assigned | None exist | DAPHNE shall support communication for RCF/RAF SLE delivery equipment
Not assigned | None exist | DAPHNE shall send user data in priority order during Automatic Delivery.

## Slide 24: Minor Changes
There are two requirements with minor wording changes.
Requirement Number | Old Requirement | Changes in highlight
NENG-OPS-013.1 | The NEN Gateway storage system shall report: the total storage available for secure/open, total storage used for secure/open, disk health for secure/open, storage system health. | DAPHNE storage system shall report: the total storage available secure/open, total storage used secure/open, disk health for secure/open, and storage system health.
NENG-PERF-002 | For NENSN scheduled supports, the NENG shall execute setup for support 120 seconds prior to activity scheduled start time | For NENSN supports, operations DAPHNE shall execute setup for operations support within 120 seconds of being commanded. prior to the scheduled start time.

## Slide 25: Suggestion to Merge and Simplify
Given the requirement for automatic failover, we feel that the intent of these 8 requirements could be fully addressed with two requirements; availability and Mean Time To Restore Full Function (MTTRFF).
Regarding MTTRFF, stating which failure is being discussed is important to understanding this requirement. We assume automatic failover has occurred and the repair brings it back to full capacity. Shipping time for repair by 566 cannot be included.
Requirement Number | Old Requirement | New Requirement
NENG-RMA-005 | The NEN Gateway nominal data processing/ delivery system shall have an availability of 0.9999 for scheduled support periods. | DAPHNE shall have an availability of 0.99 for scheduled support periods.
NENG-RMA-006 | The NEN Gateway degraded mode data processing/ delivery system shall have a delivery availability 0.9 when delivery can be made. | 
NENG-RMA-009 | The NEN Gateway data processing/ delivery system shall have a Mean Time Between Failures (MTBF) not less than 12,000 hours. | 
NENG-RMA-015 | The NEN Gateway’s Mean Time To Restore Function (MTTRF) shall be less than or equal to 48 hours. | DAPHNE's Mean Time To Restore Full Function (MTTRFF) after a first fault shall be less than or equal to 48 hours not including any shipping time.
NENG-RMA-016 | The NEN Gateway data processing/ delivery system shall have a reliability of 95% between maintenance cycles for nominal operational condition. | 
NENG-RMA-017 | The NEN Gateway data storage system shall have a reliability of 90% between maintenance cycles for nominal operational condition. | 
NENG-RMA-018 | The NEN Gateway degraded mode data processing/ delivery system shall have a reliability of 90% between maintenance cycles. | 
NENG-RMA-019 | The NEN Gateway shall comply with the NEN’s availability requirements. | 

## Slide 26
Risks

## Slide 27: Risks
There currently no project risks being maintained.
The project has one concern that it is monitoring.
  The interface to the NEN IF receiver is baselined assuming a Viasat VHR-3200 receiver. NEN has not officially selected this receiver for the mission. If another receiver is selected there will be impact to the current design, cost and schedule.

## Slide 28: Risks Matrix
1
Likelihood
Consequence
Approach
M – Mitigate
W – Watch
A – Accept
R – Research
Risk
High
Med
Low
L x C Trend
 Decreasing (Improving)
 Increasing (Worsening)
Unchanged
New risk
Index | Rank | L x C Trend | Approach | Risk Title
NONE |  |  |  | 
1 2 3 4 5
1 2 3 4 5

## Slide 29: DAPHNE Documentation Tree
Interface Control Document
Support Documentation
System and Design
LINUX NENG Users Guide
SCNS-NEN-OPI-0003
Integration Verification and Test Procedure
566-DAPHNE-TP-Rev1
Configuration Management Plan
566-DAPHNE-CMP-Rev2
Integration & Acceptance Plan & Procedures
NENG Management
Assigned
Draft
Signed
NEN ICD Between NENG and IRIS MOC
453-ICD-IRIS/NENGG
Integration and Test Plan 566-DAPHNE-TPlan-Rev1
100 %
Test Report
Software Management Plan
566-DAPHNE-SMP-Rev2
Concept of Operation
566-DAPHNE-CONOP-0001
100 %
100 %
80%
25%
0 %
100 %
NEN ICD Between NENG and M&C
453-ICD-MC-001
100 %
Requirement Specification Phase II 566-DAPHNE-REQT-008
100 %
100 %
SEMP
Risk Manag.
Safety Assur.
Software Assur.
Design and Architecture
50 %
NEN ICD Between DAPHNE and NISAR MOC
0 %
Maintenance Guide
0 %
Commissioning Plan
566-DAPHNE-CPlan-Rev1
90 %
Requirements Verification Tracability Matrix
100 %
NEN CM

## Slide 30: Requirement Management
The NENG Phase II System Requirement Document (SDR) will be under the Configuration Management of Code 453 NEN Project Configuration Control Board (CCB)
A Document Change Notice (DCN) will be issued to update the document for any approved changes.
The other documents will be maintained under DAPHNE project configuration management.

## Slide 31: DAPHNE Project Schedule
Stage | Date
SRR | 07/08/2015
DSRR | 10/01/2016
JPL Test Unit | 11/30/2016
PDR | 03/28/2017
CDR | 05/08/2017
ORR | 10/25/2017
JPL Op Unit | 01/05/2018

## Slide 32
Conclusion

## Slide 33: SRR Success Criteria DO NOT USE
Success Criteria | Comment
With respect to mission and science requirements, defined high-level program requirements are determined to be complete and are approved | 
Defined interfaces with other programs are approved | 
The program requirements are determined to provide a cost-effective program | 
The program requirements are adequately levied on either the single-program project or the multiple projects of the program | 
The plans for controlling program requirement changes have been approved | 
The approach for verifying compliance with program requirements has been approved | 
The mitigation strategies for handling identified major risks have been approved | 

## Slide 34: DSRR Success Criteria System Engineering Handbook
The project utilizes a sound process for the allocation and control of requirements throughout all levels, and a plan has been defined to complete the definition activity within schedule constraints. | 
Requirements definition is complete with respect to top-level mission and science requirements, and interfaces with external entities and between major internal elements have been defined. | 
Preliminary approaches have been determined for how requirements will be verified and validated down to the subsystem level. | 
Major risks have been identified and technically assessed, and viable mitigation strategies have been defined. | 

## Slide 35: Summary and Conclusion
Ready to start design activities
The development team has started to perform various trade studies.
  Purchased server for delivery of engineering model to NISAR November 2016.
  Preparing for speed test in conjunction with Raid vendor.
  Assisting NEN with Viasat VHR-3200 receiver function and interface.

## Slide 36
Questions?

## Slide 37
Backup

## Slide 38: Previous Architecture
Provides NEN ground station users with automated 24/7 near-real time files based IP access to spacecraft telemetry data
  NENG is composed of 4 servers (2 prime, 2 cold spares), 2 RAIDs and custom applications written in C++
  Pass Telemetry and Accounting from receiver is captured in 1 minute (nominal) files on closed system.
  Pass Telemetry and Accounting files are delivered via SCP to user facilities from closed system
  Open system is updated with Telemetry and Accounting files from closed system